## Slide 1: What is Depth of an Image?
Combination of 2D image with depth information gives us 3D image / RGBD image
RGB image
Depth image

## Slide 2: Why Do We Need Depth?
Surveillance
Drones
Robotics
Automotive
Augmented Reality
Medical imaging
3D reconstruction
3D scanning / 3D printing
3D display
3D video compression

## Slide 3: Why Do We Need Depth?
Surveillance
  China has more than 200 million surveillance cameras (1 per 7 citizens)
  USA has more than 40 million surveillance cameras (1 per 8 citizens)
  UK has more than 6 million surveillance cameras (1 per 11 citizens)
  Surveillance cameras are becoming smarter
  Computer vision tasks on 3D images perform better

## Slide 4: Why Do We Need Depth?
Drones
  Autonomous flights
  Autonomous landings
  Obstacle avoidance
  Civil applications
  Military applications
thehustle.co
www.geospatialworld.net
droneanalyst.com

## Slide 5: Why Do We Need Depth?
Robotics
  Autonomous navigation
  Obstacle avoidance
  Object grasping
  Civil applications
  Military applications
venturebeat.com
zdnet.com
bostonmagazine.com

## Slide 6: How To Extract Depth?
Left camera
Active Stereo
Left
image plane
Right
image plane
Object
Left camera
Right camera
Left
image plane
Right
image plane
Object
Structured light projector
Camera
Image plane
Object
Structured light projector
Camera
Image plane
Object
IR Laser
emitter and sensor
Structured Light
Time of Flight
Passive Stereo
Higher power consumption
Expensive
Right camera

## Slide 7: Passive Stereo
Left camera
Left
image plane
Right
image plane
Object
Passive Stereo
+ Low power
+ Low cost
+ Good accuracy
+ Good range
Higher range requires big form factor
Accuracy decreases for short range
+ Can be combined with other techniques
Target : 4K, 60 fps
4K, 30 fps
1080p, 60 fps
Zed baseline : 120 mm
Zed range : 0.5m – 20m
Zed Mini baseline : 63 mm
Zed Mini range : 0.15m – 12m
1080p, 30 fps
1080p, 30 fps
Interpupillary Distance 62mm ±10mm
Right camera

## Slide 8: Disparity
Left camera
Right camera
Left
image plane
Right
image plane
Point 1
Point 2
x2L
x2R
x1L
x1R
Baseline
Focal length
B : Baseline
F : Focal Length
x1L : Location of P1 on the left image plane
x1R : Location of P1 on the right image plane
x2L : Location of P2 on the left image plane
x2R : Location of P2 on the right image plane
xL1 – xR1 : Disparity of P1
xL2 – xR2 : Disparity of P2
We perceive depth of a 3D point based on its disparity in our left and right retinal images
Disparity is the difference in the location of the same 3D point in left and right images
Rectified images fulfil the epipolar constraint
Binocular Vision

## Slide 9: Triangulation
Left camera
Right camera
Left
image plane
Right
image plane
Point 1
Point 2
x2L
x2R
x1L
x1R
Baseline
Focal length
B : Baseline
F : Focal Length
x1L : Location of P1 on the left image plane
x1R : Location of P1 on the right image plane
x2L : Location of P2 on the left image plane
x2R : Location of P2 on the right image plane
xL1 – xR1 : Disparity of P1
xL2 – xR2 : Disparity of P2
Disparity (P1) > Disparity (P2)
(xL1 – xR1) > (xL2 – xR2)
Triangulation is the method of determining the depth from disparity
Depth is inversely proportional to disparity
Binocular Vision

## Slide 10: Depth from Disparity
z
Similar Triangles
Left camera
Right camera
P(x,z)
R(xR,f)
L(xL,f)
b
zb + z( zb - bf
-f

## Slide 11: Disparity Estimation
Left Image
Right Image
Depth Image
Local Methods
  Block Matching
  Optical Flow
  Feature Matching
Semi Global Method
Global Methods
  Dynamic Programming
  Graph Cuts
  Belief Propagation

## Slide 12: Block Matching
Left Image
Right Image

## Slide 13: Block Matching Costs
Brown, M. Z., Burschka, D., and Hager, G. D. 2003. Advances in Computational Stereo. IEEE Trans. Pattern Anal. Mach. Intell. 25, 8 (Aug. 2003), 993-1008.

## Slide 14: Rank Transform
Counts the number of pixels in the NxM filtering window that have lower intensity than the center pixel
Output is a single value ranging from 0 to NxM-1
3x3 rank transform example
38
33
35
30
37
40
39
40
36
Output of rank transform: 5

## Slide 15: Census Transform
Identifies the pixels in the NxM filtering window that have higher intensity than the center pixel
Output is a NxM-1 bit string
3x3 census transform example
38
33
35
30
37
40
39
40
36
Output of census transform:
10010100
0
0
0
0
1
1
1
0

## Slide 16: Sub Pixel Accurate Depth Estimation

## Slide 17: Depth Post Processing
Left Image
Right Image
Depth Image
Ground Truth
Irregularities
  Lack of textures
  Light reflections
  Noise
Occlusions
  Area covered behind foreground object
  Not seen in both views
Cross Check
Median
Filter

## Slide 18: 2D Median Filter
Commonly used to filter out impulsive noise from images
Can smooth out the depth map by replacing the outliers
  Irregularities in block matching will result with non-valid depth values
3x3 median filter example
58
33
35
30
37
40
39
40
36
Sorted values:
30, 33, 35, 36, 37, 39, 40, 40, 58
37
33
35
30
37
40
39
40
36

## Slide 19: Papers Implementing Median Filter
Mutual information based semi-global stereo matching on the gpu
Stereo Processing by Semiglobal Matching and Mutual Information
Real-time semi-global matching disparity estimation on the gpu
Real-time semi-global matching on the cpu
Real-time stereo vision system using semi-global matching disparity estimation: architecture and fpga-implementation
Efficient stereo matching based on a new confidence metric
Matching Cost Computation Algorithm and High Speed FPGA Architecture for High Quality Real-time Semi Global Matching Stereo Vision for Road Scenes